## Slide 1
CHAPTER 6
Information Sources & Signals
CECS 474 Computer Network Interoperability
Notes for Douglas E. Comer, Computer Networks and Internets (5th Edition)
Tracy Bradley Maples, Ph.D.
Computer Engineering & Computer Science
California State University, Long Beach

## Slide 2
Analog and Digital Signals
Data communications deals with two types of information:
    analog
    digital
Defn: An analog signal is characterized by a continuous mathematical function
    When the input changes from one value to the next, it does so by moving through all possible intermediate values.
Defn: A digital signal has a fixed set of valid levels
    When the input changes from one value to the next, each change consists of an instantaneous move from one valid level to another.

## Slide 3
Periodic and Aperiodic Signals
Signals are broadly classified as
    periodic
    aperiodic (sometimes called nonperiodic)
The classification depends on whether the signals repeat or do not repeat.
Sine Waves and Signal Characteristics
Data communications often involves the use of sinusoidal trigonometric functions:
especially sine (abbreviated sin)
We are interested in sine waves that correspond to a signal that oscillates in time:
Sine waves are important because:
    natural phenomena produce
    sine waves
    when a microphone picks up
    an audible tone, the output is
    a sine wave
    electromagnetic radiation can
    be represented as a sine waves

## Slide 4
Sine Waves and Signal Characteristics
Important characteristics of signals that relate to sine waves:
Frequency: The number of oscillations per unit time (usually seconds)
Peak amplitude: The maximum absolute value of the signal height
Peak-to-Peak amplitude: The difference between the maximum and minimum signal heights
Phase: The distance from the start of the sine wave is shifted from a reference time
Wavelength: The length of a cycle as it propagates across a medium (determined by the speed with which a signal propagates)

## Slide 5
Sine Waves and Signal Characteristics
The frequency can be calculated as the inverse of the time required for one cycle (also called the period of the wave).
Example: Using the sine wave in Figure (a):
  a period T = 1 seconds
  a frequency of 1 / T = 1 / 1 = 1 Hertz
Example: Using the sine wave in Figure (b):
  a period of T = 0.5 seconds
  its frequency is 1 / 0.5 = 2 Hertz
Notes:
Both examples are considered extremely low frequencies
Typical systems use high frequencies (often millions /second)
Engineers often express: time in fractions of a second & frequency megahertz (MHz)

## Slide 6
Composite Signals
Signals like the ones illustrated in this figure
are classified as simple:
…because they consist of a single sine wave
that cannot be decomposed further.
Most signals are classified as composite:
…because the signal can be…
    decomposed into a set of simple sine waves
    formed by adding two simple sine waves

## Slide 7
The Importance of Composite Signals and Sine Functions
Q: Why does data communications (not Computer Networking) seem obsessed with sine functions and composite signals?
A1: Signals that result from modulation are usually composite signals
A2: The mathematician Fourier discovered that it is possible to decompose a composite signal into its constituent parts into a set of sine functions, each with a frequency, amplitude, and phase.
Time and Frequency Domain Representations
Two key methods are used to represent composite signals:
1) Time Domain Representation -- A graph of a signal as a function of time
2) Frequency Domain Representation -- A graph of a signal made up of every simple frequency included.
• The y-axis gives the amplitude, and the x-axis gives the frequency

## Slide 8
Example: The function asin(2πt) is represented by a single line of height a that is positioned at x = t
Time Domain Representation
Frequency Domain Representation
Advantages of the Frequency Domain Representation:
    It can be used with nonperiodic signals
    It is compact

## Slide 9
Bandwidth of an Analog Signal
Defn: Analog bandwidth is the difference between the highest and lowest frequencies of the constituent parts of the signal (i.e., the highest and the lowest frequencies obtained by Fourier analysis)
Figure 6.7 shows a Frequency Domain plot with frequencies measured in Kilohertz (KHz)
Such frequencies are in the range audible to a human ear.
In the figure, the bandwidth is the difference between the highest and lowest frequency (5 KHz - 1 KHz = 4 KHz)
In analog telephone systems, the usable frequency range is 300 Hz to 3400 Hz range

## Slide 10
Digital Signals and Signal Levels
Some systems use voltage to represent digital values:
    Make a positive voltage correspond to a logical one
    zero voltage correspond to a logical zero
For example, +5 volts can be used for a logical one and 0 volts for a logical zero
If only two levels of voltage are used, each level corresponds to one data bit (0 or 1)
Some physical transmission mechanisms can support more than two signal levels,
When multiple digital levels are available each level can represent multiple bits.
For Example: consider a system that uses four voltage levels:
-5 volts, -2 volts,
+2 volts, +5 volts
Each level can correspond to two bits of data as in Figure 6.8 (b).

## Slide 11
Digital Signals and Signal Levels
The relationship between the number of levels required and the number of bits to be sent is straightforward:
There must be a signal level for each possible combination of bits
There are 2n combinations possible with n bits
NOTE: Practical electronic systems cannot distinguish between signals that differ by arbitrarily small amounts. Thus, practical systems are restricted to a few signal levels.

## Slide 12
Baud and Bits Per Second
Q: How much data can be sent in a given time?
A: The answer depends on two aspects of the communication system.
the number of signal levels
the amount of time the system remains at a given level before moving to the next (the number of signal changes per second)
Baud and Bits Per Second
Defn: The baud rate is how many times the signal can change per second.
For example: If a system requires the signal to remain at a given level for 0.001 seconds, we say that the system operates at 1000 baud
Thus, both the baud rate and the number of signal levels control the bit rate of a system.

## Slide 13
Synchronization and Agreement About Signals
The electronics at both ends of a physical medium must have circuitry to measure time precisely and synchronize with the data as it arrives.
Example: If one end transmits a signal with 10 elements per second, the other end must expect exactly 10 elements per second.
Building electronic systems that agree at the high speeds used in modern networks is extremely difficult.
A fundamental issue that arises from the way data is represented concerns synchronization of sender/receiver.
Line Coding
Several techniques are used to help with synchronization errors.
In general, there are two broad approaches:
  Before transmitting, the sender transmits a known pattern of bits (typically a set of alternating 0s and 1s) for receiver to use in synchronization
  Data is represented in such a way that synchronization is included in the encoding
The term line coding is used to describe the way data is encoded in a signal.

## Slide 14
Manchester Encoding Used in Computer Networks
Manchester Encoding is used with Ethernet
Why? Because detecting a transition in signal level is easier
than measuring the signal level
So Manchester Encoding uses transitions rather than levels to define bits
In Manchester Encoding,
a 1 corresponds to a transition from negative voltage level to a positive voltage level
a 0 corresponds to a transition from a positive voltage level to a negative level
The transitions occur in the middle of the time slot of a bit.

## Slide 15
Converting an Analog Signal to Digital
Many sources of information are analog:
  which means they must be converted to a digital form for further processing (e.g., before they can be encrypted)
There are two basic approaches:
  pulse code modulation (PCM)
  delta modulation (DM)
In PCM, the level of an analog signal is measured repeatedly at fixed time intervals and converted to digital form.
In DM, the changes in the levels of an analog signal are measured repeatedly at fixed time intervals and converted to digital form. (Not discussed further here.)

## Slide 16
Converting an Analog Signal to Digital
The three steps used in PCM for telephony:
sampling -- each measurement is known as a sample
quantization -- a sample is quantized by converting it into a small integer value, called a quanta. The range of the signal from the minimum to maximum levels is divided into a set of quanta. Typically, a power of 2 values.
encoding -- the quantized sample is encoded into a specific format
Converting an Analog Signal to Digital Using PCM for Voice

## Slide 17
The Nyquist Theorem and Sampling Rate
An analog signal must be sampled in PCM (or DM).
How often should an analog signal be sampled?
Taking too few samples (undersampling) means that the digital values only give a crude approximation of the original signal
Taking too many samples (oversampling) means that more digital data will be generated, which uses extra bandwidth
The mathematician Nyquist determined the answer to the question of how much sampling is required:
sampling rate = 2* fmax
  where fmax is the highest frequency in the composite signal.
Nyquist’s Theorem provides a practical solution to the problem:
Sample a signal at least twice as fast as the highest frequency that must be preserved

## Slide 18
Nyquist Theorem and Telephone System Transmission
The telephone system was designed to transfer voice.
Measurements of human speech have shown that preserving frequencies between 0 - 4000 Hz provides acceptable audio quality.
Thus, when converting a voice signal from analog to digital the signal should be sampled at a rate of 8000 samples per second.
The PCM standard used by the phone system quantifies each sample into:
An 8 bit value for quality
  the range of input is divided into 256 possible levels so that each sample has a value between 0 and 255
The rate generated for a single telephone call is:

## Slide 19
Encoding and Data Compression
Data compression refers to a technique that reduces the number of bits required to represent data.
Data compression is relevant to communication systems because reducing the number of bits used to represent data reduces the time required for transmission.
A communication system can be optimized by compressing data
There are two types of compression:
Lossy - some information is lost during compression
Lossless - all information is retained in the compressed version
Lossy compression is generally used with data that a human consumes, such as an image, video/audio

## Slide 20
Encoding and Data Compression
The key idea is that the compression only needs to preserve details to the level of human perception:
a change is acceptable if humans cannot detect the change
Example: JPEG (used for images) compression or MPEG-3 (abbreviated MP3 and used for audio recordings) employ lossy compression
Lossless compression preserves the original data without any change
lossless compression can be used for documents or in any situation where data must be preserved exactly
arbitrary data can be compressed by a sender and decompressed by a receiver to recover an exact copy of the original
(Chapter 29 discusses compression in more detail)